## Slide 1: Effectiveness of risk management process towards error reduction in the laboratory at Sakra World Hospital
AUTHORS:
Dr. Shabnam Roohi
Mr. Deepak Agarkhed

## Slide 2: Introduction
60–70% of the most important clinical decisions are based on laboratory test results.
The risk of inappropriate patient care due to laboratory errors ranges from 6.4% to 30%.
Introduction of risk management strategies in the form of failure mode effect analysis (FMEA) into the laboratory arena should allow us to identify the risk of errors and to reduce the errors that are more likely to affect patient outcomes.

## Slide 3: Failure Mode and effects analysis ( FMEA)
A systematic way of examining a design prospectively for possible ways in which failure can occur.
It assumes that no matter how knowledgeable or careful people are, errors will occur in some situations and may even be likely to occur.
Source:JCI :5th edition

## Slide 4: Target
The FMEA target is to measure the risk probability of any possible failure or nonconformity (NC), by an index, called risk priority number (RPN) that is the product of:
  The ‘‘Effect severity (S)” from 1 to 4
  The ‘‘Failure occurrence (O)”, from 1 to 5
  The ‘‘Failure detection (D)’’ from 1 to 4.
The RPN can go from a minimum of 1 (1 X 1 X 1) to a maximum of 80 (4 X 5 X 4) as per the risk quantification scoring adopted by us.

## Slide 5
Risk quantification |  | 
Effect severity (S) |  | 
Score | Severity description | 
4 | Catastrophic | 
3 | Critical | 
2 | Moderate | 
1 | Minor | 
Failure occurrence (O) |  | 
Score | Occurrence characteristics | Description of occurrence probability
5 | Continuous | Daily
4 | Frequent | Weekly
3 | Occasional | Monthly
2 | Uncommon | It may occur within 1 to 6 weeks
1 | Remote | It may occur annually
Failure detection (D) |  | 
Score | Description of detection mechanisms | 
4 | The existing mechanisms will not identify | 
3 | Controls are partial | 
2 | Current controls would detect immediate failures, but they are not fail-safe | 
1 | Certain of detecting the failure before affecting the patient | 

## Slide 6: Objectives of the Study
To identify the potential errors that may occur in the laboratory.
To establish the impact of the various errors on patient test results
To prioritize the high impact errors and take appropriate corrective actions
To analyse the effectiveness of the corrective actions taken in reducing the errors
Implement modifications to laboratory procedures as appropriate.

## Slide 7: Materials and methods
The laboratory process mapping into preanalytical, analytical and post analytical.
Data collection:
  Direct observation
  Incident/ NC reports.
All potential risks listed out in FMEA form.
Brainstorming sessions with the stake holders for allotment of RPN score before starting the study and after implementation of corrective actions taken.

## Slide 8: Materials and methods
The potential risks with an RPN of more than 30 were identified for risk mitigation.
The risk quantification was again performed 6 months after implementation of corrective measures.
The difference in the RPN score before and after each corrective action was implemented was considered for determining the effectiveness of the corrective actions taken.

## Slide 9: Process mapping
Pre analytical
Step 1: Accommodation and safety
Step 2: Equipment, reagents and consumables
Sub process 1: Indenting of supplies.
Sub process 2: Ordering of supplies.
Sub process 3: Receiving supplies.
Sub process 4: Storage of supplies
Step 3: Sample collection
Step 4: Sample transport
Analytical
Step 1: Quality assurance
Step 2: Analysis
Post analytical
Step 1: Result transfer
Step 2: Report generation
Sub process 1,2,3 …
Sub process 1,2,3….
Sub process 1,2,3,…
Sub process 1: result checking
Step 3: Report release
Sub process 1: critical result information
Sub process 2….
Sub process 2: result calculation
Sub process 3: result transcription

## Slide 10
FMEA Form
RPN = S X O X D

## Slide 11: Results
80 potential risks were identified.
10 areas with RPN score of more than 30 were identified and appropriate corrective actions were implemented.
The repeat risk quantification for the identified risks revealed a reduction in the RPN scores by 20% to 90%.

## Slide 12: Initial risk quantification and proposed action
Process step | FAILURE MODE | SEVERITY | OCCURANCE | DETECTION | RPN | EFFECT | ACTION
Pre analytical-step 2 | Delay in receiving consumables from main store | 3 | 5 | 4 | 60 | Delay in treatment due to non availability of diagnostic reports in time. | SOP for receipt of items changed and implemented.
Pre analytical: Step 3 | Test not billed on current date | 2 | 5 | 4 | 40 | Delay in treatment. Inconvenience to patients | One month previous date to be selected for viewing of results in HIS
Pre analytical: Step 2 | Reagent not available | 3 | 4 | 3 | 36 | Delay in treatment due to non availability of diagnostic reports in time. | Buffer stock and reorder level (ROL) for a reagents ad consumables defined.
Pre analytical: Step 4 | Delay in transport from accession to lab | 3 | 5 | 2 | 30 | Loss of stability of specimen leading to repeat collection. | Training.

## Slide 13: Initial risk quantification and proposed action
PROCESS STEP | FAILURE MODE | SEVERITY | OCCURANCE | DETECTION | RPN | EFFECT | ACTION
Post analytical: Step 3 | Critical report not informed | 4 | 4 | 3 | 48 | Delay in treatment leading to loss of life. | Improve detection control by strict monitoring and audit of all critical results.
Post analytical Step 2 | Results not seen on bulk verification screen | 3 | 5 | 3 | 45 | Delay in treatment. Inconvenience to patients | Modification done in the LIS
Post analytical: Step 2 | Calculation error | 3 | 4 | 3 | 36 | Inappropriate treatment if not detected or Delay in treatment if detected. | Calculated parameters interfaced
Post analytical: Step 2 | Transcription error | 3 | 4 | 3 | 36 | Inappropriate treatment if not detected or Delay in treatment if detected. | Automated tests interfaced. Pre typed but editable templates inserted into the result entry screen of LIS.

## Slide 14: Initial risk quantification and proposed action
PROCESS STEP | FAILURE MODE | SEVERITY | OCCURANCE | DETECTION | RPN | EFFECT | ACTION
Post analytical: Step 2 | Abnormal results not delta checked | 3 | 4 | 3 | 36 | Inappropriate treatment if not detected or Delay in treatment if detected | Delta check to be incorporated into the LIS
Pre analytical: Step 1 | Aerosol | 3 | 5 | 2 | 30 | Injury to the personnel. | Training and use of PPE

## Slide 15: Post implementation
Table 2 EFFECT OF IMPROVEMENT ACTION ON RPN |  |  |  | 
FAILURE MODE | BEFORE | AFTER | % IMPROVEMENT | OBSERVATION
Delay in receiving store | 60 | 6 | 90 | Change in the process brought down the frequency and improved detection, but severity remained the same.
Critical report not informed | 48 | 16 | 67 | Change in the detection protocol brought down the frequency, but severity remained the same.
Results not seen on bulk verification screen | 45 | 6 | 87 | Correction in HIS, frequency brought down.
Test not billed on current date | 40 | 20 | 50 | Change in the detection protocol brought down the frequency, but severity remained the same.
Reagent not available | 36 | 12 | 67 | Change in the process & detection protocol brought down the frequency, but severity remained the same.

## Slide 16: Post implementation
Table 2 EFFECT OF IMPROVEMENT ACTION ON RPN |  |  |  | 
FAILURE MODE | BEFORE | AFTER | % IMPROVEMENT | OBSERVATION
Calculation error | 36 | 6 | 83 | Automation of the process reduced frequency
Transcription error | 36 | 6 | 83 | Automation of the process reduced frequency
Abnormal results not delta checked | 36 | 12 | 67 | Change in the detection protocol brought down the frequency, but severity remained the same.
Delay in transport from accession to lab | 30 | 24 | 20 | Change in the detection protocol brought down the frequency, but severity remained the same.
Aerosol | 30 | 18 | 40 | Change in the detection protocol brought down the frequency, but severity remained the same.

## Slide 17: Discussion
FMEA as a preventive technique well known in some areas of healthcare but at a nascent stage in the laboratory.
We encountered a few difficulties during the implementation of FMEA related to:
  The time and manpower consumption for detailed analysis of the processes and data.
  The difficulty in getting all stakeholders in a single platform for brainstorming.

## Slide 18: Conclusion
The improvement potentially obtainable by FMEA in a clinical laboratory is high, and this fact should suggest further experiences in this field.

## Slide 19
Thank you